Experiment 9th:
Goal: introduction to LPF and HPF, cutoff frequency,

filter is a system that only lets desired signals through while blocking other signals	or weakening them

the high pass filter will pass any signal below its frequency and will block any signal above
while the low pass filter does the exact opposite

cutoff frequency is the frequency in which gain of circuit compared to gain of dc falls by coef of sqrt(2)

first we bind this circuit with the following attributes
R=4.7K, C=33nf
then we power our circuit with a sinus wave with peak of 4 volts and 1hz

first part:
frequency	100	200	500	750	1k	2k
V(p-p_0)